## Slide 1
Ultrasound evaluation of hip synovitis (PIUS project)
Daniel Windschall, Ralf Trauzeddel, Faekah Gohar, Hatice Adiguzel-Dundar, Sven Hardt, Manuela Krumrey-Langkammerer, Lampros Fotis5, Rainer Berendes, Sebastian Schua, Maria Haller, Ferhat Demir, Betul Sözeri, Silvia Magni-Manzoni on behalf of the PReS Imaging Working Party
60 JIA patients were enrolled. 76 hips with and 32 hips without clinical arthritis as well as data from 449 healthy hips was analyzed. Interobserver reliability of BM and PD positivity (grading >1) showed substantial agreement (kappa 0.74). BM was positive in 71/76 of hips with clinical arthritis (93%, sensitivity 0.97 (0.93-1.0), specificity 0.85 (0.74-0.97) versus 2/32 (6 %) in hips without arthritis. PD positivity had only a frequency of 6 (8%) in hips with versus 0 (0%) in hips without arthritis. Anterior recess size (mean+SD) was significantly wider in patients with clinical arthritis (9.9+2.5 vs 5.5+1.3, p-value 0.001). Articular capsule and femoral head cartilage thickness did not differ between patients with and without arthritis.
The Pediatric Internationally agreed UltraSound Hip synovitis protocol (PIUS-hip) could be limited to one longitudinal scan including B-Mode scoring plus measurement of anterior recess size for maximal sensitivity for synovitis. The anterior recess size as measured bone to capsule distance, was significantly higher in hips with clinical synovitis than control joints from the same patients, and compared to presumed healthy controls. Higher BM grading positivity (grade > 2) was a significant sign for hip joints with clinical arthritis. Measurement of the anterior and posterior capsule layers and cartilage thickness were unhelpful for determining hip involvement. Unusual compared to other joints, the finding of PD positivity is a rare finding in MSUS of the hip joint in JIA and should therefore not be used as a marker for hip affection.
Trauzeddel RF, Lehmann H, Windschall D, et al. Age-dependent arthrosonographic reference values of the hip joint in healthy children and adolescents - a cross-sectional multicenter ultrasound study. Pediatr Radiol. 2017;47:1329–36. doi: 10.1007/s00247-017-3862-5
Windschall D, Trauzeddel R, Gohar F. et al. Development and validation of a pediatric internationally agreed ultrasound knee synovitis protocol (PIUS-knee) by the PReS imaging working party. Pediatr Rheumatol Online J. 2024;22:94. doi: 10.1186/s12969-024-01029-4
Clinic for Pediatric and Adolescent Rheumatology
Rheumatologisches Kompetenzzentrum Nordwestdeutschland
Introduction
The PIUS project (Pediatric Internationally consented UltraSound protocols) of the PreS imaging working party aims to develop homogeneous and most sensitive musculoskeletal ultrasound (MSUS) examination protocols for all pediatric joints
Methods
Consecutive JIA patients with clinically confirmed hip arthritis underwent an MSUS-protocol, consented by the Pediatric Rheumatology european Society (PReS) Imaging Working Party, which included the longitudinal anterior recess view for the evaluation of synovitis using the pediatric OMERACT grading score for B-Mode (BM) and Power-Doppler Mode (PD) views, measurement of the recess size and measurement of the articular capsule thickness. In the transverse plane, femoral head thickness was recorded. Interobserver reliability of BM and PD was first tested
Results
Aims
PIUS-Hip-Protocol
References
Conclusions
To evaluate the sensitivity of pediatric musculoskeletal ultrasound (MSUS) for the detection of hip arthritis in patients with juvenile idiopathic arthritis (JIA) and secondly, to measure the articular capsule thickness and femoral head cartilage thickness in hip joints with and without arthritis.
Table 1: B-Mode and Power-Doppler-Mode findings in the anterior longitudinal view hip joints with and without clinical arthritis
Table 2: B-Mode and Power-Doppler-Mode positivity in the anterior longitudinal view of hips with and without arthritis